NON-SHALLOW SPHERICAL SHELLS

Bakur Gulua*, Lali Tibua**

*Iv. Javakhishvili Tbilisi State University, I.Vekua Institute of Applied Mathematics, Tbilisi, Georgia, bak.gulua@gmail.com

**Sokhumi State University, Tbilisi, Georgia, lali.tibua@mail.ru

In this paper we consider non-shallow spherical shells [1]. By means of I. Vekua method two-dimensional system of equations is obtained. Using the method of the small parameter approximate solutions of I. Vekua’s equations is constructed. The small parameter, where  is the thickness of the shell,  is the radius of the sphere. Using complex variable functions concrete problem has been solved, when the components of external force are constant.

Acknowledgement. This work was supported by ...

References

- Vekua, I.N.: Shell Theory: General Methods of Construction. Pitman Advanced Publishing Program, Boston-London-Melbourne, 1985.